## Slide 1: CA216 - Scheduling
Brendan Simms - 19500949

## Slide 2: Process Speeds
My implementation of a turn around time and wait time calculation within the round robin scheduling algorithm did not work correctly as I did not include a metric to measure the start time of a process which is important for round robin as processes are not always completed in their first run. So I will be excluding this when comparing my sorting algorithms.
In general the fastest algorithm was the Shortest Job First algorithm when using Average wait time and Average turnaround time as metrics for measuring performance.
The worst performing algorithm was, in general, the First-Come-First-Served algorithm although there were instances where its performance matched that of Shortest-Job-First and Priority scheduling.

## Slide 3: Exceptions
Exceptions occurred when Burst time and priority for all tasks were equal to one another
When Burst time was the same across all tasks this caused Shortest-Job-First to have the same turnaround time and wait time as First-Come-First-Served
The same situation arose for Priority scheduling when priority values were the same for every task
This was because the algorithm no longer sorted by the intended metric as the metric for all tasks were the same causing the algorithms to essentially become a First-Come-First-Served algorithm

## Slide 4: Round Robin
As previously mentioned my wait time and turnaround time metrics for round robin did not implement correctly and there is several reasons I concluded caused this:
The final task burst time was being added to the total wait time.
The process did not take into account the fact that these process do not complete before moving onto the next task like the other sorting algorithms for this project.

## Slide 5: List implementation
To read the contents of the file into a list I simply used a for loop to read the lines and split them using the split() function separating them by using the “ , “ which was contained in each text file.
I used a regular list containing a tuple, [tasknumber, priority, CPU_burst], to store the information. I did this to allow the information for a task all accessible from one entry point, the tuple containing the information.

## Slide 6: My List: Positives vs Negatives
Using python lists had both positives and negatives:
Positives:
Python Lists are easy to manipulate
Allowed access to built in functions such as sort() and reverse() which made it easy to order the processes for specific algorithms
Data was easily stored as tuples meaning all information could be called by simply calling said tuple
Negatives:
Using Lists containing tuples meant that maths operands couldn’t easily be applied to the information which made the Round Robin algorithm particularly tricky.

## Slide 7: Thank you for listening!